## Slide 1
ANNOUNCE / BUSINESS
HW 01 (due Th, 01/16)
NEW STUFF
Why is stress a tensor?
What exactly is a tensor?
Stress transformation
Mohr’s circle (with example)
Advanced Mechanics

## Slide 2
Stress
Shear stress subscripts:
  first refers to surface acting on
  second to direction

## Slide 3: Stress
Stress is a 3-D quantity
“Stress state” is commonly represented graphically using an infinitesimal cube
Two categories of stress: normal () and shear ()
Traction vector (“stress vector” in textbook) on each face:
  Components depend on coordinate system (like vectors)

## Slide 4: Stress Tensor
Stress is a second-order tensor (and can be represented as a matrix)
  Again, components depend on coordinate system
The matrix of stresses is symmetric (e.g., , etc)
  6 possible unique components; 3 normal, 3 shear
A vector is a first-order tensor

## Slide 5
=
Stress Tensor
Indicial notation (Einstein summation convention) – Practice this!

## Slide 6
Quiz
A
B
C
D
Which stress tensor accurately describes the stress state shown?
Notes: Correct answer is B

## Slide 7
Stress – Special Cases
Uniaxial, biaxial stress (no shear -> principal stress state)
Triaxial stress (no shear; principal stress state)
  when all 3 are equal: equitriaxial, spherical, hydrostatic
Plane stress (figures a and b)
Pure shear (figure c)
What does the stress tensor look like for each of the above?

## Slide 8
Stress Equations

## Slide 9
Variation of Stress Through Body
Equilibrium requires …
3-D Version
differential form of
Eq’ns constrain stress variations and body forces
Notes: Allow stress to vary over element, expressing increase in stress using Taylor Series expansion
Sum moments around corner to show equivalence of shear stresses within plane
Sum forces in each direction

## Slide 10
Variation of Stress Through Body
Consider stress distribution in a hanging bar, loaded by its own weight
Notes: Consider bar hanging under its own weight
Or consider example of cantilever bending: derivative of normal stress with respect to x (axis of beam) must be equal and opposite to derivative of transverse shear stress with respect to y (through beam thickness)

## Slide 11
Stress on Inclined Sections
Notes: Demonstrates that stress components change as we change the coord sys they refer to

## Slide 12
Stress on Inclined Sections
Note
  stress components change with coordinate system even though loading does not change
  results are achieved by force equilibrium, not stress equilibrium (no such law)
Notes: Demonstrates that stress components change as we change the coord sys they refer to

## Slide 13
Stress on Inclined Sections
Prelude to stress transformation

## Slide 14
Stress Transformation – Plane Stress

## Slide 15
Stress Transformation – Plane Stress
Remember: Stress does not change during transformation, but its components change in the different coordinate system
(note that are stresses here, but balance law is applied to force)
Notes: p, sigma, and tau are all stresses here, but equilibrium requires equality of force, so areas are also considered; hence, the first set of equations between p and sig and tau
These are the equations that define Mohr’s Circle

## Slide 16
Invariants
It can be shown that
or … the sum of the normal stresses is invariant, i.e. it does not change with θ
also true in 3-D, as we will see
another way to say this: the trace of the stress tensor is invariant
Familiar invariant example: recall that the length of a vector (its magnitude) does not change when it is represented in a new coordinate system. We thus say that vector magnitude is invariant.

## Slide 17
Principal Stress
Normal and shear stresses are continuously variable with theta (even though the stress state is not changing)
Normal stress is at extreme when shear stress is zero. This stress is called the principal stress (and is invariant).
Principal stress and max shear stress always occur 45 degrees apart

## Slide 18
Principal Stress
Derive equations for principal stresses by taking the derivative of the stress transformation equations and setting equal to zero. This gives the angle at which extreme values occur.
Two solutions for θp! → 2 principal stresses (in 2-D)
Plugging into stress transformation equations gives
(subscripts 1 and 2 used to denote principal stresses)

## Slide 19
Maximum Shear Stress
We can similarly find the equation for max shear stress
Principal stresses, i.e. eigenvalues of the (2D) stress tensor

## Slide 20
Mohr’s Circle
Alternative to memorizing long equations … Mohr’s Circle
Example: The state of plane stress at a point on the surface of the airplane fuselage is represented on the element oriented as shown. Represent the state of stress at the same point on an element that is oriented 30° clockwise from this position.
Notes: My conventions for Mohr’s Circle:
Shear stress axis positive downward – preserves rotation direction (CCW still positive)
Sign of shear stress in stress state is defined by considering direction of rotation stress causes on element, again using right hand rule